## Slide 1
BayWa
WindLens
01 / 07 DETECT
Find the gap
A missing interval is evidence of missing telemetry — not proof of why production stopped.
TURBINE T1 · SHOWN WINDOW
healthy
gap
healthy
WHAT YOU CAN RELY ON
The outage window shown for this record comes directly from BayWa’s own data.
WHAT TO CHECK YOURSELF
A gap does not identify the cause. Confirm sensor fault vs. mechanical outage independently.
WindLens · Evidence-first reconstruction
01 / 07

## Slide 2
BayWa
WindLens
02 / 07 SELECT
Pick a reference turbine
Behavior first. Geography only as a plausibility check.
T1 target
O1
O2
H5
pre-outage history
SELECTED REFERENCE
O1 · holdout R² 0.419 · 8,424 paired observations
LIMITATION
No turbine-location registry exists in this BayWa dataset.
WindLens · Evidence-first reconstruction
02 / 07

## Slide 3
BayWa
WindLens
03 / 07 ESTIMATE
Reconstruct wind, then power
1
Reference wind
O1 reports
wind readings.
2
Target wind
Fit a transparent
measure–correlate–predict line.
3
Target power
Apply T1’s own
pre-outage power curve.
4
Lost energy
Integrate expected
power into kWh.
A calculation you can inspect end to end: every number traces back to a real reading.
CHECK BEFORE REUSE
No single method wins everywhere. Review alternative methods before assuming this is universal.
WindLens · Evidence-first reconstruction
03 / 07

## Slide 4
BayWa
WindLens
04 / 07 GATE
Check the result before trusting it
01
Input quality
Are the source readings usable?
02
Reference overlap
Does the reference explain the target?
03
Tested range
Is this inside validated conditions?
04
Completeness
Are enough points reconstructed?
05
Calibration
Does uncertainty behave honestly?
A gate is not a guarantee. It is an honest boundary around the number.
RULE
Failed or unevaluated checks stay visible.
WindLens · Evidence-first reconstruction
04 / 07

## Slide 5
BayWa
WindLens
05 / 07 EVIDENCE
Three tiers, never one number
TIER 1 / BASELINE
6.8%
WAPE
Same-farm single-turbine reconstruction
same-farm baseline
TIER 2 / CEILING
8.8%
WAPE
Whole-site masking stress test
same-farm stress test
TIER 3 / FLOOR
13.9%
WAPE
Distant cross-farm backtest (external data: Kelmarsh vs. Penmanshiel)
cross-farm floor proxy
The questions differ, so the numbers stay separate.
WindLens · Evidence-first reconstruction
05 / 07

## Slide 6
BayWa
WindLens
06 / 07 LIMITS
What this cannot tell you yet
The evidence brackets distance — it does not close the neighbouring-farm gap.
Tier 1
~0.5 km
same-farm baseline
Tier 2
<1 km
stress-test ceiling
Tier 3
~399 km
cross-farm floor
UNTESTED GAP
2–100 km
HONEST BOUNDARY
The BayWa challenge’s actual whole-farm / neighbouring-farm scenario remains untested by this prototype.
WindLens · Evidence-first reconstruction
06 / 07

## Slide 7
BayWa
WindLens
07 / 07 OPPORTUNITIES
What we would build next
01
Calibrated uncertainty interval
More held-out BayWa data to build one honestly.
02
Automatic outage-cause classification
Separate sensor faults from real mechanical outages.
03
A genuine neighbouring-farm test
A verified nearby second farm — not a distant proxy.
BUILD
WITH
EVIDENCE
WindLens prototype · October 2026
WindLens · Evidence-first reconstruction
07 / 07